## Slide 1: Home Energy Digital Twin
Professional walkthrough: model, results, UX, and operational flow
Date: 2026-02-08

## Slide 2: Presentation scope
1. Digital twin from first principles
2. Data architecture and offline-first runtime
3. Controller logic and physical constraints
4. Detailed results and graph diagnostics
5. Tesla-style energy and money flow visuals
6. Deployment and upgrade path

## Slide 3: First principles model
Per 5-minute interval:
- Baseline cost = load x price
- Scenario cost = import x price - export x price + degradation
- Savings = baseline - scenario
Physical layers:
- PV output from irradiance and temperature
- Battery SoC dynamics with power and reserve constraints
- Dispatch controller selects charge/discharge/export actions

## Slide 4: Assumptions used
PV assumptions:
- 10 kW nameplate, PR 0.82
- Temp coefficient -0.004 / degC
Battery assumptions:
- 10 kWh capacity, 1 kWh reserve, initial 5 kWh
- 5 kW charge/discharge/export limits
- 90% round-trip efficiency
- Degradation term 0.02 AUD/kWh discharged

## Slide 5: Data and runtime architecture
Inputs:
- Amber usage/prices (SQLite cache + Supabase history)
- Open-Meteo irradiance near Vaucluse NSW
Execution:
- backtest mode and 5-minute live mode
- writes simulation_intervals + simulation_runs to SQLite
Dashboard APIs:
- /api/simulation/status
- /api/simulation/intervals
- /api/simulation/flow

## Slide 6: Controller comparison summary
Latest cached run highlights:
- Optimizer: today +0.0576 AUD, MTD +0.2538 AUD, next24h +0.0394 AUD
- Rule: today +0.0000 AUD, MTD -0.1903 AUD, next24h +0.0030 AUD
Interpretation:
- Optimizer captures price spreads better in this window
- Rule thresholds are easier to interpret but less adaptive

## Slide 7: Daily savings by controller
Sydney-day aggregate view of interval savings.

## Slide 8: Cumulative savings trajectory
Running savings total over the backtest window.

## Slide 9: Cost and savings breakdown
Baseline vs scenario cost and resulting net savings.

## Slide 10: Energy movement totals
Import, charge, discharge, export and PV totals by controller.

## Slide 11: Battery dynamics (optimizer)
State-of-charge and interval charge/discharge behavior.

## Slide 12: Interval savings heatmap
Optimizer interval savings by Sydney 30-minute slot.

## Slide 13: Flow mockup: midday solar surplus
Design objective from Tesla/Home Assistant references:
- separate connection ports to avoid ambiguous center crossings
- directional energy arrows + dedicated money row

## Slide 14: Flow mockup: evening peak support
Battery-to-home path dominates while grid top-up is explicitly smaller.

## Slide 15: Flow mockup: overnight arbitrage charge
Grid-to-battery charging path is isolated from grid-to-home path for clarity.

## Slide 16: Dashboard UX changes delivered
Main dashboard:
- stronger hierarchy, premium card styling, clearer status chips
- simulation status integrated in Data Status panel
Simulation dashboard:
- Tesla-style live flow board
- money flow cards (import/export/net/savings)
- stale indicators and as_of surfaced in header

## Slide 17: Operational behavior
Live simulation job:
- run_simulation_live.py every 5 minutes
- cache-first writes to SQLite simulation tables
API behavior:
- always includes as_of and stale flags
- supports offline dashboard reads
- avoids blocking UI when upstream APIs are unavailable

## Slide 18: Recommended next upgrades
1. Deterministic weather fallback (clear-sky + cached blend)
2. Optional LP/MILP optimization backend
3. Network tariff and feed-in asymmetry modeling
4. EV/V2H coupling scenarios
5. Automated reconciliation report to validate savings confidence

## Slide 19: Reproducibility commands
.venv/bin/python scripts/run_scenario_simulation.py --mode backtest --controller optimizer --site-id 01J061Q7Q883JF26YMGZVVTMV9 --start 2025-12-28T00:00:00Z --end 2025-12-31T00:00:00Z
.venv/bin/python scripts/run_scenario_simulation.py --mode backtest --controller rule --site-id 01J061Q7Q883JF26YMGZVVTMV9 --start 2025-12-28T00:00:00Z --end 2025-12-31T00:00:00Z
MPLBACKEND=Agg MPLCONFIGDIR=/tmp .venv/bin/python scripts/generate_simulation_presentation_pngs.py
.venv/bin/python scripts/generate_flow_mockup_pngs.py
.venv/bin/python scripts/export_simulation_pptx_with_keynote.py